Format		Summary of Operation	Instruction Code	Execution States	T Bit
AND	Rm,Rn	Rm & Rm → Rn	0010nnnnmmmm1001	1	—
AND	#imm,R0	R0 & imm → R0	11001001iiiiiiii	1	—
AND.B	#imm,@(R0,GBR)	(R0+GBR) & imm → (R0+GBR)	11001101iiiiiiii	4	—

Description
This instruction ANDs the contents of general registers Rn and Rm and stores the result in Rn.
This instruction can be used to AND general register R0 contents with zero-extended 8-bit
immediate data, or, in indexed GBR indirect addressing mode, to AND 8-bit memory with 8-bit
immediate data.

Notes
With AND #imm,R0, the upper 24 bits of R0 are always cleared as a result of the operation.

Operation
  AND(long m, long n) /* AND Rm,Rn */
  {
    R[n]&=R[m];
    PC+=2;
  }

  ANDI(long i) /* AND #imm,R0 */
  {
    R[0]&=(0x000000FF & (long)i);
    PC+=2;
  }

  ANDM(long i) /* AND.B #imm,@(R0,GBR) */